## Slide 1
COMPUTER NETWORKS — SEMESTER PROJECT
University Campus
Network Design
& Implementation
Cisco Packet Tracer Simulation
Air University, Kamra | BS CS F’24 - B
Wasif Ali - 245187
Labs (x4)
Classrooms (x2)
Faculty Office
HOD Office
Exam Office
Server Room
10 Network Zones

## Slide 2
Presentation Agenda
01
Project Overview & Objectives
02
Network Topology Design
03
IP Addressing Scheme
04
Routing & Fault Tolerance
05
Server Room & Services
06
Email & Wireless
07
Access Control Lists (ACLs)
08
Testing & Challenges
09
Conclusion

## Slide 3
Project Overview
What did we build?
A fully functional university campus network simulated in Cisco Packet Tracer — covering the entire university building with multiple departments, servers, and security policies.
7
Routers
10
Subnets
100+
End Devices
8
Servers
6
ACL Policies
2
WAPs

## Slide 4
Network Topology Design
Hybrid Star-Ring Topology
Core Layer
Central 2911 Router — backbone connected to all 6 zone routers via serial links
Distribution Layer
6x Zone Routers (2911 + HWIC-2T) interconnected in a ring using DCE/DTE serial cables
Access Layer
Cisco 2960 Switches per zone — connecting all end devices
Zone Router Assignments
Router | Zone Covered
Left Side | Lab 1 + Lab 2
Right Side | Lab 3 + Lab 4
Mid-Upper | Faculty + HOD
Upper Side | Top Classrooms
Mid-Lower | Server + Exam
Lower Side | Bottom Classrooms

## Slide 5
IP Addressing Scheme
All devices use Static IP Addressing — for predictability, easy debugging, and full control.
LAN Subnets
Zone | Subnet | Gateway
Lab 1 (Left) | 192.168.10.0/24 | 192.168.10.1
Lab 2 (Left) | 192.168.20.0/24 | 192.168.20.1
Lab 3 (Right) | 192.168.30.0/24 | 192.168.30.1
Lab 4 (Right) | 192.168.40.0/24 | 192.168.40.1
Faculty Office | 192.168.50.0/24 | 192.168.50.1
Top Classrooms | 192.168.60.0/24 | 192.168.60.1
Exam Office | 192.168.70.0/24 | 192.168.70.1
Bottom Class. | 192.168.80.0/24 | 192.168.80.1
HOD Office | 192.168.90.0/24 | 192.168.90.1
Server Room | 192.168.100.0/24 | 192.168.100.1
WAN Links (Router-to-Router)
Central ↔ Each Zone
10.1.X.0/30 (6 links)
Ring: Left ↔ Mid-Upper
10.0.1.0/30
Ring: Mid-Upper ↔ Top
10.0.2.0/30
Ring: Top ↔ Right
10.0.3.0/30
Ring: Right ↔ Mid-Lower
10.0.4.0/30
Ring: Mid-Lower ↔ Bottom
10.0.5.0/30
Ring: Bottom ↔ Left
10.0.6.0/30
/30 = 255.255.255.252 | Only 2 usable IPs per link — perfect for point-to-point

## Slide 6
Routing & Fault Tolerance
Why Static Routing?
Predictable and deterministic packet paths
Easier to debug in a lab environment
No routing protocol overhead
Full manual control over primary and backup paths
Floating Static Routes — 3-Level Failover
AD Value | Path Type | Activates When
AD = 1 | Primary — via Central Router | Always (Central is UP)
AD = 10 | Backup 1 — via Ring Neighbor A | Central Router DOWN
AD = 20 | Backup 2 — via Ring Neighbor B | Central + Neighbor A DOWN
Lower AD = Higher Priority. Router automatically switches to backup path when primary fails — no manual intervention needed.

## Slide 7
Server Room Configuration
Subnet: 192.168.100.0/24 | Gateway: 192.168.100.1 | Connected to: Mid-Lower Router | Access: Unrestricted for all zones
DNS Server
192.168.100.10 | DNS Resolution for all domains
www.chatgpt.com
192.168.100.60 | HTTP Web Hosting
www.claude.ai
192.168.100.70 | HTTP Web Hosting
www.yahoo.com
192.168.100.20 | HTTP Web Hosting
google.com
192.168.100.30 | HTTP Web Hosting
www.aack.au.edu.pk
192.168.100.40 | HTTP Web Hosting
www.classroom.google.com
192.168.100.50 | HTTP Web Hosting
Email Server
192.168.100.10 | SMTP (Port 25) / POP3 (Port 110)
IT Manager PC
192.168.100.5 | Network Management

## Slide 8
Email Service & Wireless Access
Email Service
Domain:
aack.au.edu.pk
Server IP:
192.168.100.10
SMTP Port:
25 (Sending)
POP3 Port:
110 (Receiving)
Example User:
L1PC1@aack.au.edu.pk
HOD User:
HODCS@aack.au.edu.pk
All PCs configured with Incoming (POP3) and Outgoing (SMTP) mail server settings for cross-zone email communication.
Wireless Access Points
2 WAPs deployed for demonstration of wireless connectivity concept:
WAP 1
Lab 01 Area
Subnet: 192.168.10.0/24 | Connected to: Left Zone Switch
WAP 2
Exam Office
Subnet: 192.168.70.0/24 | Connected to: Mid-Lower Switch
Each WAP shares the same subnet and gateway as wired devices in its zone — no extra routing needed.

## Slide 9
Access Control Lists (ACLs)
ACLs enforce a realistic university access hierarchy — protecting sensitive offices from unauthorized access.
Access Policy Matrix
Source \ Dest | Server Room | Faculty | HOD | Exam
Labs / Classrooms | ✅ | ✅ | ❌ | ❌
Faculty Office | ✅ | — | ✅ | ❌
HOD Office | ✅ | ✅ | — | ✅
Exam Office | ❌ | ❌ | ✅ | —
Server Room | — | ✅ | ✅ | ✅
ACL Placements
PROTECT-HOD → Mid-Upper (in)
PROTECT-EXAM → Mid-Lower (in)
LABS-LEFT → Left Router (in)
LABS-RIGHT → Right Router (in)
TOP-RESTRICT → Upper (in)
BOTTOM-RESTRICT → Lower (in)
FACULTY-RESTRICT → Mid-Upper (in)
HOD-OUTBOUND → Mid-Upper (out)
⭐ HOD Design Choice: HOD can initiate contact with Labs & Classrooms (one-way). Labs CANNOT reply back. This models real university hierarchy — HOD broadcasts, students cannot directly reach HOD.

## Slide 10
Testing & Verification
Test | Source | Destination | Result
Cross-zone Ping | Lab 1 PC24 | Faculty Office PC7 | PASS
Server Access | Lab 1 PC24 | IT Manager (100.10) | PASS
DNS Resolution | Any Lab PC | www.yahoo.com | PASS
HTTP Web Access | Any Lab PC | google.com page | PASS
ACL: Labs → HOD | Lab PC | HOD Office PC | BLOCKED
ACL: Faculty → HOD | Faculty PC | HOD Office PC | PASS
ACL: Exam → HOD | Exam PC | HOD Office PC | PASS
Failover Test | Lab 1 PC | Faculty PC (Central DOWN) | PASS via Ring
All 8 test scenarios passed — network fully functional and verified end-to-end.

## Slide 11
Challenges & Solutions
⚠ HWIC-1GE-SFP not linking up
✓ Switched to HWIC-2T serial ports for all router-to-router connections
⚠ IR8340 had Layer 2 switch ports
✓ Replaced with standard 2911 — used serial links to central instead
⚠ Serial link IP overlap (/8 mask)
✓ Corrected to 255.255.255.252 (/30) — eliminated all overlaps
⚠ Ring backup causing routing loop
✓ Rebuilt all routes with correct ring order and verified next-hops
⚠ ACL blocking HOD reply from Labs
✓ Made intentional — HOD initiates (one-way), Labs cannot reply to HOD
⚠ Teammate IP addressing errors
✓ Manually corrected all IPs and gateways across all zones
⚠ Broadcast ping 192.168.X.255 failing
✓ Used directed ping to specific host IPs — confirmed all zones reachable

## Slide 12
Conclusion
What we achieved:
✓ Scalable campus network with 10 isolated subnets across a full university building
✓ Fault-tolerant ring topology with 3-level floating static route failover
✓ Full DNS + HTTP server infrastructure with 7 hosted domains
✓ Internal email service (SMTP/POP3) for cross-zone university communication
✓ ACL-based security policy modelling real university access hierarchy
✓ Wireless access points demonstrating mobile device connectivity
Air University, Kamra | BS CS F’24 - B| Computer Networks Project